## Slide 1: TIMES-DK Indutry Sectors
Model structure and how to update files

## Slide 2: Structure if the industry sectors in TIMES-DK
The model has 12 sectors that is mirrored in the CGE model
Each sector demands some energy services and there are 8 different services coming in 3 groups
Electricity demands
  Appliances
  Motors
Heat demands
  High temperature heat
  Medium temperature heat
  Room heat
Haulage (internal transport)
  Tractors, trucks, fishing boats
  Forklifts
  Forest machines

## Slide 3
Industry sectors
Agriculture
Food
Chemical
Glas&Concrete
Metal
Other
Motor vehicles
Sales
Private service
Public service
Contruction
Other Utilities
Medium temp. heat
High temp. heat
Heating
Light and Electronics
Electric motors
Electricity
District heat
Oil
Gas
Biomass
Bio-fuels
Tractors, trucks, fishing boats
Forklifts
Forest machines
Others
Energy Services

## Slide 4: File structure for industry

## Slide 5: Calibrating VT_DK_IND
The industry sector is calibrated to the Danish Energy Matrixes. This can cause a small diviation from the Energy Statistics.
As the data fed into the base year template (VT-file) is based on the Energy Matrixes, then it is only capacity and full load hours that needs to be adjusted when updating data.

## Slide 6: Updating the base year template VT_DK_IND
Output from Danish Energy Matrix is used to create base year consumption for IntERACT5 sectors (INTERACT5 - Aggregering af IO-tabeller.xlsx).
The output table from above is copied to VT_DK_IND sheet "Energy Matrix".
Final energy consumption divided on services are created from VMAS2015 database (Alle matricer Final_VMAS2015_Pivo.xlsb). This includes all industry sectors except Public Sector which was not a part of the VMAS2015 study.
Comparing detailed fuel consumption for Public Sector with fuel consumption for different Private Sector industries shows that Public Sector in shares looks like "Arts, Entertainment and Recreation activities" which has sector nummer 56 in VMAS2015 study (See Alle matricer Final_VMAS2015_Pivo.xlsb, sheet "Public sector shares"). Based on this the shares for VMAS sector 56 is used to represent Public service energy service shares.
Table with energy consumption from "Alle matricer Final_VMAS2015_Pivo.xlsb", table from sheet "Pivo Aggr 1" is copied (with no links) to VT_DK_IND sheet "Pivo Aggr 1".

## Slide 7: Subres_IND_Energy

## Slide 8: Subres_IND_Energy_Trans